## Slide 1: Analog I/O

## Slide 2
Arduino boards contain a multichannel, 10-bit analog to digital converter.
It will map input voltages between 0 and the operating voltage(5V or 3.3V) into integer values between 0 and 1023.
This yields a resolution between readings of: 5 volts / 1024 units or, 0.0049 volts (4.9 mV) per unit.
The ESP32 has 2 x 12-Bit SAR (Successive Approximation Register) ADC hardware peripherals that can read 18 different analog input channels.
The ADC firmware driver API supports ADC1 (8 channels, attached to GPIOs 32 – 39), and ADC2 (10 channels, attached to GPIOs 0, 2, 4, 12 – 15, and 25 – 27).
The voltage measured is then assigned to a value between 0 and 4095, in which 0 V corresponds to 0, and 3.3 V corresponds to 4095.
NOTE:
ADC2 is used by the Wi-Fi driver. Therefore the application can only use ADC2 when the Wi-Fi driver has not been started.
Some of the ADC2 pins are used as strapping pins (GPIO 0, 2, 15) thus cannot be used freely.

## Slide 3: Reading Analog Values
To read analog Value from any analog pin, use analogRead()
Pin is the name of the analog input pin to read from.
Returns the analog reading on the pin.

## Slide 4: Other Inbuilt Functions
analogReadResolution(resolution): set the sample bits and resolution. It can be a value between 9 (0 – 511) and 12 bits (0 – 4095). Default is 12-bit resolution.
analogSetWidth(width): set the sample bits and resolution. It can be a value between 9 (0 – 511) and 12 bits (0 – 4095). Default is 12-bit resolution.
analogSetCycles(cycles): set the number of cycles per sample. Default is 8. Range: 1 to 255.
analogSetSamples(samples): set the number of samples in the range. Default is 1 sample. It has an effect of increasing sensitivity.
analogSetClockDiv(attenuation): set the divider for the ADC clock. Default is 1. Range: 1 to 255.

## Slide 5
analogSetAttenuation(attenuation): sets the input attenuation for all ADC pins. Default is ADC_11db. Accepted values:
  ADC_0db: sets no attenuation. ADC can measure up to approximately 800 mV (1V input = ADC reading of 1088).
  ADC_2_5db: The input voltage of ADC will be attenuated, extending the range of measurement to up to approx. 1100 mV. (1V input = ADC reading of 3722).
  ADC_6db: The input voltage of ADC will be attenuated, extending the range of measurement to up to approx. 1350 mV. (1V input = ADC reading of 3033).
  ADC_11db: The input voltage of ADC will be attenuated, extending the range of measurement to up to approx. 2600 mV. (1V input = ADC reading of 1575).

## Slide 6
analogSetPinAttenuation(pin, attenuation): sets the input attenuation for the specified pin. The default is ADC_11db. Attenuation values are the same from previous function.
adcAttachPin(pin): Attach a pin to ADC (also clears any other analog mode that could be on). Returns TRUE or FALSE result.
adcStart(pin), adcBusy(pin) and resultadcEnd(pin): starts an ADC convertion on attached pin’s bus. Check if conversion on the pin’s ADC bus is currently running (returns TRUE or FALSE). Get the result of the conversion: returns 16-bit integer.

## Slide 7: ADC Voltage Reference
The ADC reference voltage (VREF) varies between different chips.
By design, the ADC reference voltage of ESP32 is 1100 mV, however, the true reference voltage can range from 1000 mV to 1200 mV.
For Arduino Boards, the options are:
  DEFAULT: the default analog reference of 5 volts (on 5V Arduino boards) or 3.3 volts (on 3.3V Arduino boards)
  INTERNAL: a built-in reference, equal to 1.1 volts on the ATmega168 or ATmega328P and 2.56 volts on the ATmega32U4 and ATmega8 (not available on the Arduino Mega)
  INTERNAL1V1: a built-in 1.1V reference (Arduino Mega only)
  INTERNAL2V56: a built-in 2.56V reference (Arduino Mega only)
  EXTERNAL: the voltage applied to the AREF pin (0 to 5V only) is used as the reference.

## Slide 8: How to change ADC Voltage Reference
type: which type of reference to use
NOTE: It can get more complex. We will stop for now

## Slide 9: Analog Output using PWM (Pulse Width Modulation)
Pulse Width Modulation, or PWM, is a technique for getting analog results with digital means.
Digital control is used to create a square wave, a signal switched between on and off. This on-off pattern can simulate voltages in between the full Vcc of the board and off (0 Volts) by changing the portion of the time the signal spends on versus the time that the signal spends off.
The duration of "on time" is called the pulse width.
To get varying analog values, you change, or modulate, that pulse width.
If you repeat this on-off pattern fast enough with an LED for example, the result is as if the signal is a steady voltage between 0 and Vcc controlling the brightness of the LED.

## Slide 10: Multiple Buttons Using Analog Input
Use a resistor network as voltage dividers.
Let each button feed a different voltage to the analog pin.
By detecting the voltage we can tell which button has been pressed.

## Slide 11: Circuit

## Slide 13: analogWrite()
Writes an analog value to a pin using PWM.
Can be used to light a LED at varying brightnesses or drive a motor at various speeds.
After a call to analogWrite(), the pin will generate a steady rectangular wave of the specified duty cycle until the next call to analogWrite() (or a call to digitalRead() or digitalWrite()) on the same pin.
pin: the Arduino pin to write to. Allowed data types: int.
value: the duty cycle: between 0 (always off) and 255 (always on). Allowed data types: int.

## Slide 14: Analog Output Using DAC
DAC (digital to analog converter) is a very common peripheral used to convert a digital signal to an analog form.
ESP32 and ESP32-S2 have two 8-bit DAC channels. The DAC driver allows these channels to be set to arbitrary voltages

## Slide 15: dacWrite
This function is used to set the DAC value for a given pin/DAC channel.
pin GPIO pin.
value to be set. Range is 0 - 255 (equals 0V - 3.3V).

## Slide 16: dacDisable
This function is used to disable DAC output on a given pin/DAC channel.
pin GPIO pin.