## Slide 1: Accessing EEPROM and Flash Memory

## Slide 2
EEPROM is basically used to store the non volatile data which is required to be stored even if there is power loss or controller resets.
Memory whose values are kept when the board is turned off (like a tiny hard drive).
Arduino and Genuino boards have different amounts of EEPROM: 1024 bytes on the ATmega328P, 512 bytes on the ATmega168 and ATmega8, 4 KB (4096 bytes) on the ATmega1280 and ATmega2560.
Functions in the EEPROM class is automatically included with the platform for your board, meaning you do not need to install any external libraries.

## Slide 3
To use this library
From here, you can read or write to different memory addresses in the EEPROM

## Slide 4: Read
Reads a byte from the EEPROM. Locations that have never been written to have the value of 255.
address: the location to read from, starting from 0 (int)
Returns the value stored in that location (byte)

## Slide 5: Write:
Write a byte to the EEPROM.
Address: the location to write to, starting from 0 (int)
value: the value to write, from 0 to 255 (byte)
It does not return any value.
The EEPROM memory has a specified life of 100,000 write/erase cycles, so you may need to be careful about how often you write to it.

## Slide 6: Update
Write a byte to the EEPROM. The value is written only if differs from the one already saved at the same address.
Address: the location to write to, starting from 0 (int)
value: the value to write, from 0 to 255 (byte)

## Slide 7: Get
Reads any data type or object from the EEPROM.
address: the location to read from, starting from 0 (int)
data: the data to read, can be a primitive type (eg. float) or a custom struct
Returns a reference to the data passed in

## Slide 8: Put
Write any data type or object to the EEPROM.
address: the location to write to, starting from 0 (int)
data: the data to write, can be a primitive type (eg. float) or a custom struct

## Slide 9: ESP 32 Flash Memory
How to store and read values from the ESP32 flash memory using Arduino IDE.
The data saved in the flash memory remains there even when the ESP32 resets or when power is removed.
Data can be read from flash as many times as you want
You can use up to 512 bytes in the flash memory.
This means you have 512 different addresses, and you can save a value between 0 and 255 in each address position.

## Slide 10: Using Flash Memory on ESP 32
Include the EEPROM Library
You define the EEPROM size. This is the number of bytes you’ll want to access in the flash memory.
Initialize the EEPROM Library with the defined size.

## Slide 11: Write
To write data to the flash memory, you use the EEPROM.write() function that accepts as arguments the location or address where you want to save the data, and the value (a byte variable) you want to save:
After the write command, use commit to save the data.

## Slide 12: Read
To read a byte from the flash memory, you use the EEPROM.read() function.
This function takes the address of the byte you want to read as an argument.