## Slide 1: WIFI Connection, Transmitting Data through WiFI via HTTP (GET/POST), Simple Web server

## Slide 2: WiFi Connection
All Routers (most especially Wireless routers) need the right credentials to be able to connect to them.
You need the SSID and the PASSWORD to connect.
You must know these two things

## Slide 3: Steps to Connecting to a WiFi
Import the necessary library
Type out your SSID and Password
Begin connection using function begin

## Slide 4: To check for Successful Connection
Use status function to check if the connection is successful
This code checks if connection has not been achieved and prints “.” till it is achieved

## Slide 5: Print out IP Address
Use localIP function to get the IP address
It returns the IP address

## Slide 6: HTTP Get
GET is used to request data from a specified resource.
Note that the query string (name/value pairs) is sent in the URL of a GET request:

## Slide 7
GET requests can be cached
GET requests remain in the browser history
GET requests can be bookmarked
GET requests should never be used when dealing with sensitive data
GET requests have length restrictions
GET requests are only used to request data (not modify)

## Slide 8: Steps for Get
Import the necessary libraries (HTTPClient)
If you want to use WiFi connection, Import libraries for WiFi
Secure your connection to the network
Create an instance of HTTPClient

## Slide 9
Start the connection to the server using begin function
Begin takes the server path… (the url of the website you want to reach).
Send the http get request using get function. This returns the response code. Check standard response code for more info

## Slide 10
Check if the response code is what you want (here, we just check if it is greater than 0)
Get the response string
Do what you like with the string… For example, you can print it on the screen

## Slide 11
End the connection.

## Slide 12: HTTP Post
POST is used to send data to a server to create/update a resource.
The data sent to the server with POST is stored in the request body of the HTTP request:

## Slide 13
POST requests are never cached
POST requests do not remain in the browser history
POST requests cannot be bookmarked
POST requests have no restrictions on data length

## Slide 15: Steps for Post
Import the necessary libraries (HTTPClient)
If you want to use WiFi connection, Import libraries for WiFi
Secure your connection to the network
Create an instance of HTTPClient

## Slide 16
Start the connection to the server using begin function
You can also use WiFiClient in the begin function
Begin takes the server path… (the url of the website you want to reach).

## Slide 17
Add the HTTP Headers
Send HTTP Post Data using the post function
Http Request data is a string containing the data e.g
String httpRequestData = "api_key=tPmAT5Ab3j7F9&sensor=BME280&value1=24.25&value2=49.54&value3=1005.14";

## Slide 18: Post JSON Object
If you want to use JSON in your post data, add the header too before using the http post function.

## Slide 19: Post Plain Text
If you want to send plain text or a value, add the header:
Then add the http post function

## Slide 20: Simple Web Server Using ESP
A WebSocket is a persistent connection between a client and a server that allows bidirectional communication between both parties using a TCP connection.
This means you can send data from the client to the server and from the server to the client at any given time.
The client establishes a WebSocket connection with the server through a process known as WebSocket handshake.
The handshake starts with an HTTP request/response, allowing servers to handle HTTP connections as well as WebSocket connections on the same port.
Once the connection is established, the client and the server can send WebSocket data in full duplex mode.

## Slide 22
Using the WebSockets protocol, the server (ESP32 board) can send information to the client or to all clients without being requested.
This also allows us to send information to the web browser when a change occurs.
This change can be something that happened on the web page (you clicked a button) or something that happened on the ESP32 side like pressing a physical button on a circuit.

## Slide 23: The Simple Website hosted on ESP 32 (Server)

## Slide 24
The ESP32 web server displays a web page with a button to toggle the state of GPIO 2;
For simplicity, we’re controlling GPIO 2 – the on-board LED. You can use this example to control any other GPIO;
The interface shows the current GPIO state. Whenever a change occurs on the GPIO state, the interface is updated instantaneously;
The GPIO state is updated automatically in all clients. This means that if you have several web browser tabs opened on the same device or on different devices, they are all updated at the same time.

## Slide 26: What happens when you click on the “Toggle” button:
  Click on the “Toggle” button;
  The client (your browser) sends data via WebSocket protocol with the “toggle” message;
  The ESP32 (server) receives this message, so it knows it should toggle the LED state. If the LED was previously off, turn it on;
  Then, it sends data with the new LED state to all clients also through WebSocket protocol;
  The clients receive the message and update the led state on the web page accordingly. This allows us to update all clients almost instantaneously when a change happens.

## Slide 27: We Will be needing 2 Libraries
ESPAsyncWebServer
AsyncTCP

## Slide 28: Steps
Import necessary libraries
Set up necessary wifi connections

## Slide 29
Create object for the server and the websocket
Put your HTML/CSS/Javascript code in Program memory (the code is very long.

## Slide 30
Initialize websocket
Set the route for the webpage
Start the server.

## Slide 31: Handle WebSocket Messages
The handleWebSocketMessage() function is a callback function that will run whenever we receive new data from the clients via WebSocket protocol
void handleWebSocketMessage(void *arg, uint8_t *data, size_t len) {
AwsFrameInfo *info = (AwsFrameInfo*)arg;
if (info->final && info->index == 0 && info->len == len &&
info->opcode == WS_TEXT)
{
data[len] = 0;
if (strcmp((char*)data, "toggle") == 0) {
ledState = !ledState; notifyClients();
}
}
}
If we receive the “toggle” message, we toggle the value of the ledState variable. Additionally, we notify all clients by calling the notifyClients() function. This way, all clients are notified of the change and update the interface accordingly.

## Slide 32: Configure the WebSocket server
Now we need to configure an event listener to handle the different asynchronous steps of the WebSocket protocol. This event handler can be implemented by defining the onEvent() as follows:

## Slide 33
void onEvent(AsyncWebSocket *server, AsyncWebSocketClient *client, AwsEventType type, void *arg, uint8_t *data, size_t len) {
switch (type) {
case WS_EVT_CONNECT:
Serial.printf("WebSocket client #%u connected from %s\n", client->id(), client- >remoteIP().toString().c_str());
break;
case WS_EVT_DISCONNECT:
Serial.printf("WebSocket client #%u disconnected\n", client->id());
break;
case WS_EVT_DATA:
handleWebSocketMessage(arg, data, len);
break;
case WS_EVT_PONG:
case WS_EVT_ERROR:
break;
}
}

## Slide 34
The type argument represents the event that occurs. It can take the following values:
WS_EVT_CONNECT when a client has logged in;
WS_EVT_DISCONNECT when a client has logged out;
WS_EVT_DATA when a data packet is received from the client;
WS_EVT_PONG in response to a ping request;
WS_EVT_ERROR when an error is received from the client.

## Slide 35: Initialize WebSocket
The initWebSocket() function initializes the WebSocket protocol.

## Slide 36: processor()
The processor() function is responsible for searching for placeholders on the HTML text and replace them with whatever we want before sending the web page to the browser.
In our case, we’ll replace the %STATE% placeholder with ON if the ledState is 1. Otherwise, replace it with OFF.